## Slide 1: Embedded 2 – Cosy cafetaria Corona presentation
By Tobias Cromheecke, Thomas Feys, Robin Van de Poel, Arthur Van den Storme
16-4-2020

## Slide 2: Index
Power management
Microcontroller
Sensors
Code
Wi-Fi communication
Software design

## Slide 3: Power management
Completed:
Battery: Lithium-Ion battery
Charger IC
Protection IC
Reverse polarity protection circtuit
LDO: 3,7 V to 3,3 V
Load switches to turn on/off the sensors
Availability to measure current via wire to put a currentprobe on or sense resistor
To do:
Soldering
Testing
Designing revision

## Slide 4: Problems/limitations
Delay times for deliveries due corona measures
Lack of tools/instruments to solder and for testing:
  Most power management IC’s have an exposed pad which needs a solder oven to solder properly
  Lack of oscilloscope etc.

## Slide 5: Wi-Fi communication
Completed:
Data transfer between ESP32 and Python server
Faster connection setup because of static IP => reduced power consumption
To do:
Process received data in Python
Measure power consumption
Test connection with actual sensor data instead of dummy data
Test Python server on Raspberry Pi instead of laptop

## Slide 6: Software design
Completed:
Entering and wakeup from deep sleep
Save variables in RTC memory so that they are retained after deep sleep
NTP synchronisation for time information => disable sensors at night
To do:
Put the individual pieces of software in one general structure
Test the system
Power measurements

## Slide 7: Problems/limitations
No ability to fully disable sensors with load switch until the final PCB is ready
No ability to measure power consumption
Difficult to test full system because sensors, Raspberry Pi and ESP32-SOLO are not all available to one person